Pool Filter Cartridge Cleaning Instructions

When should a cartridge element be cleaned?

For swimming pools, clean the cartridge when filter canister pressure reaches 10-12 PSI above the initial system or new cartridge starting pressure. Cartridges should be chemically cleaned in Filter Cleaner at the end of every season before they are put away for winter or anytime you have had to treat the pool for an algae bloom.

What is the procedure to clean my cartridge?

- Remove the cartridge from the filter housing following the manufacturer’s instructions.

- Use a garden hose with a straight flow nozzle to wash down the filter element.  Work from the top down, holding the nozzle at a 45o angle, and wash all the pleats with emphasis between pleats. Never use a pressure washer as this will damage the filter.

- Rinse until all dirt and debris is gone.

- For all swimming pool filters where perspiration, suntan lotions, and other oils are present, soak the element for at least six hours (overnight is most effective) in a commercial filter cleaner (Filter Cleaner).

- For pool filters add half a bottle of Filter Cleaner for each filter to approximately 20L of water. Ensure that the entire filter is submersed in the solution and soak overnight.

- Rinse the cartridge again to remove oils and cleaning solution.

- Let the cartridge air dry completely before installing it back into the filter housing or storing for winter.

# Text boxes

597 Garner Rd E, Ancaster, ON   L9G 3K9

(905)648-7727    www.budsspas.com