HELPFUL TIPS TO KEEP IN MIND WHEN

MAINTAINING YOUR POOL!

NEW POOL OR NEW LINER CUSTOMERS: PLEASE BRING IN A WATER SAMPLE (IN THE SAMPLE BOTTLE PROVIDED) TO BUDS SPAS AND POOLS BEFORE ADDING ANY CHEMICALS AND/OR BEFORE ENTERING YOUR POOL FOR THE FIRST TIME.

1. Test kits or strips can help you monitor your pool water, however, we recommend visiting Bud’s Spas & Pools for a more comprehensive water test at least once a month to maintain proper water balance. Monthly tests are required to ensure that the warranties on your pool equipment and pool liner remain valid. Additionally, at home testing should be done on a weekly basis to ensure bather safety, comfort, and proper sanitation. If any problems occur (ex. algae or cloudy water), or if you question the balance of your water, bring a water sample in for testing.

2. Before adding chemicals to your pool water, the pump needs to be running. To maintain proper filtration, water quality, and clarity, the pump should be operating 24 hours a day. If your pump is on a timer, you should make sure that it runs during the hottest hours of the day. A minimum time of 8-12 hours of circulation is recommended.

3. When adding chemicals, proper dosage is very important. To avoid cloudy water, please be sure to wait the recommended time required between each chemical addition.

4. Follow the 3 step weekly maintenance program printed out on the bottom of each water test. You should also be adding a weekly dose of Meta-Stain Prevent especially if you have a heater.

The 3 step maintenance program consists of: Aqua Foot (Sanitizer), Zap Shock (Oxidizer), and End Algi-pro 40 (Algaecide).

We recommend performing the following procedures when using a:

- Chlorinator : Add 1-2 Aqua Foot and replace them as they dissolve, (checking them once a week). Set your chlorinator dial at 2 ½ and adjust as needed to keep a reading of 1-3ppm.

- Brominator: Fill the feeder half full with Brominating Tablets and set the dial at 2 and adjust as needed to keep a reading of 1-3ppm.

You should always be checking your sanitizer level and adjusting the dial on your chlorinator/brominator as required (depending on use, weather conditions, etc.)

Shocking and oxidizing eliminates bather wastes such as perspiration, body oils, and cosmetics that tend to cloud the water and use up free chlorine. Shocking and oxidizing will help eliminate these wastes. In addition to your weekly routine, a shock or oxidizer should be added after heavy use (ex. a party) or after heavy rainfall.

*Please remember to remove all toys, automatic vacuums etc from the pool before shocking and leave your solar blanket off for at least 8 hours after shocking.

5. Stabilizer is an important chemical that needs to be added to all pools to prevent sanitizer loss due to the sun. Stabilizer is also added to ensure that the liner is protected and that the liner warranty remains valid.

6. Do not leave the solar blanket on your pool for an extended period of time, as it facilitates a warm environment that algae thrives in. The best time to put on the solar blanket is at night and for a maximum of 12 hours. The solar blanket is meant prevent heat loss, it will not heat the pool.

7. A dirty filter can cause many problems in your pool such as foaming, cloudiness, poor circulation, and an increased amount of chemicals needed to clear the water. We recommend using Filter Cleaner at least once a season OR after an algae problem to prevent these problems from occurring. These cleaners will also help control scale/rust and remove oils/greases from the filter.

a. If you have a cartridge filter, please remember to rinse the filter off periodically through the season and/or when pressure gets too high, cleaning between each fiber strip. Do not use a pressure washer as it could damage the fibers.

b. If you have a sand filter, the media should be changed every 3-5 years and possibly sooner if it has not been chemically cleaned each season.

8. Over time o-rings tend to break down and as a result can cause an improper seal with your pump, heaters, etc. Apply a silicone lubricant to o-rings at the beginning and end of every pool season to prevent this from happening (or as needed through the season). Using something other than a silicone based lubricant (ex. Vaseline) can lead to o-rings breaking down faster.

9. Things you should be doing on a regular basis:

- Brush down the walls and floor once a week and before vacuuming to stir up any debris or algae that may be hiding.

- Clean out your skimmer and pump baskets often, as it can restrict the flow and use up sanitizer if there is a lot debris gathering in the baskets.

- Suction side automatic vacuums are a great way to keep your water clean, but they should not be used for any longer than 6 hours. The water at the surface is not circulating when the vacuum is in use.

- Bring a water test once a month to Bud’s or whenever you are having problems with your pool water.

# Text boxes

597 Garner Rd E, Ancaster, ON   L9G 3K9

(905)648-7727 or (905)529-5323   www.BudsSpasAndPools.ca